## Slide 1
Sławomir Nowaczyk, Thorsteinn Rögnvaldsson, Stefan Byttner
Fredrik Bode, Niclas Karlsson, Rune Prytz
ReDi2Service & In4Uptime

## Slide 2: Predictive Maintenance
“Plannable” downtimes
  avoid high consequential costs for unplanned stops
Shorter workshop visits
  better planning and diagnostics
  reduce number of incorrect repairs
Optimization of maintenance intervals
  based on needs of individual vehicles
Increase knowledge about vehicles and their usage

## Slide 3: Business Model Change
“In future, all companies will be software companies”
  George Colony, CEO of Forrester Research
Automotive industry is moving products to services
  but this will require fundamental shift in business models
In particular, there is a need to improve things quickly
  software as the medium allows much faster innovation cycles
A development cycle has to be based on actual data
  following “Build – Measure – Learn” model

## Slide 4: The Uptime Problem
Vehicles are becoming more and more complex
  we need better diagnostic and fault detection systems
Building specialised diagnostic functions is expensive
  it is unrealistic to expect that for each individual fault
Real usage data shows actual problems to look for
  sometimes what is “known” turns out to be wrong
What is important to focus on changes with age
  we need continuous monitoring and life-long learning

## Slide 5: Two Approaches
Classical supervised machine learning
  research problems arise from the specifics of the data
Self-organising, unsupervised knowledge discovery
  create a system that can “understand” its own operation
Predictive
Maintenance
Vehicle
Data
Explaining
Deviations
Predictive
Maintenance
Interesting
Faults
Vehicle
Data

## Slide 6: Self-Monitoring System
We have a “sniffer” on-board every vehicle
  it learns the data characteristics (model) of that vehicle
Those models are then compared between vehicles
  discovering what is normal/abnormal for a particular fleet
Detected deviations are then matched against repairs
  to find out which faults (if any) can be responsible
The goal is to increase vehicle uptime
  a self-monitoring system should, with time, become an “expert” that can highlight interesting patterns in the data

## Slide 7: Targeted Diagnostics
23% overlap (142 examples)
Data based on Alen Atamer (2004) Comparison of FMEA and Field-Experience for a Turbofan Engine with Application to Case-Based Reasoning, IEEE Aerospace Conference.
FMEA
anticipated
failure modes
(610 examples)
Faults
encountered
in the field
(727 examples)

## Slide 8: The Leap

## Slide 10: Learning Fleet
System automatically finds signals to analyse
  from on-board data and fault information
System defines what is normal and what is not
  warns about detected deviations and irregularities
  identifies possible faults by linking against service records
Learns characteristics of faults that actually happen
  can present and explain them to workshop personnel
It is not as reliable nor accurate as focused diagnostic
  it is designed to support, not replace, experts

## Slide 11
Air admission blocked
Injector blocked
Expert defines what to look at and what is normal
  identifies factors relevant for each possible fault
This approach works very well and is reliable
  but does not scale sufficiently well
Classical Approach

## Slide 12: Fleet-based Approach

## Slide 13: Fleet-based Approach

## Slide 14: Long-term pilot study
Over 3 years (since fall 2011)
19 Volvo buses (8500 model)
  14 from year 2007
  5 from year 2008/2009
  driven about 100,000 km/year each
In service around Kungsbacka
  rotating routes and drivers
We are logging ~100 signals
  at 1 Hz frequency
  around 500MB/week/bus of data`

## Slide 15: The VACT system (Volvo Analysis and Communication Tool)
DynaFleet hardware
  software developed in
  the ReDi2Service project
Communication
  GPS, GPRS modem
  3 CAN interfaces
  USB memory
Easy to configure onboard logging capabilities
  as well as on-line data analysis functions

## Slide 16: Fleet Histograms
Distances between histograms
  of Engine Oil Temperature
  19 different vehicles
  during one week in 2011
Histograms are evenly distributed:
nothing strange
Each point corresponds to a bus observation
(illustrated using multidimensional scaling)

## Slide 17: Fleet Histograms
We are looking for a vehicle that is different from rest of the group
By analysing the VSR: consistent deviation of bus 378 is caused by a broken ECU...
Cooling fan runs at full speed all the time

## Slide 18: Bus 70452
2009 model

## Slide 19: Bus 70452
2009 model
Sep
2011
Jan
2012
Jul
2013
Jan
Gear box problems
(Nov 28)
Coolant system leak (Dec 5)
Problems with Strocco heater
(Dec 9 & Jan 30)
Tampering with EBS system (”sabotage”) Volvo Action Service
(Feb 10)
Oil pressure problems (Mar 2)
Complaints that engine „runs strangely” Probable cause: CAC leak
(Apr 12)
Service before annual inspection
(inspection
Apr 24)
Engine ”knocks”. Cylinder 1 jams during annual
inspection.
(Repair May 4)
Problems with alternator belt tension (Jul 30)
Service
(Oct 8)
Gear box not working, replaced or repaired
(Nov 26)

## Slide 20: Bus 70452 – The Data
Temperature Upstream Catalyst is higher for a long period of time, and keeps growing

## Slide 21
Those two temperatures both show significantly abnormal characteristics since November 2011
Both those deviations
disappear in May 2012
Notes: Combine 28 and 29

## Slide 22: Bus 70452
2009 model
Sep
2011
Jan
2012
Jul
2013
Jan
Gear box problems
(Nov 28)
Coolant system leak (Dec 5)
Problems with Strocco heater
(Dec 9 & Jan 30)
Tampering with EBS system (”sabotage”) Volvo Action Service
(Feb 10)
Oil pressure problems (Mar 2)
Complaints that engine „runs strangely” Probable cause: CAC leak
(Apr 12)
Service before annual inspection
(inspection
Apr 24)
Engine ”knocks”. Cylinder 1 jams during annual
inspection.
(Repair May 4)
Problems with alternator belt tension (Jul 30)
Service
(Oct 8)
Gear box not working, replaced or repaired
(Nov 26)

## Slide 23: Bus 70452
The CAC repair April 12, 2012, is probably an erroneous repair
The CAC was not the problem
Sep
2011
Jan
2012
Jul
2013
Jan
Gear box problems
(Nov 28)
Coolant system leak (Dec 5)
Problems with Strocco heater
(Dec 9 & Jan 30)
Tampering with EBS system (”sabotage”) Volvo Action Service
(Feb 10)
Oil pressure problems (Mar 2)
Complaints that engine „runs strangely” Probable cause: CAC leak
(Apr 12)
Service before annual inspection
(inspection
Apr 24)
Engine ”knocks”. Cylinder 1 jams during annual
inspection.
(Repair May 4)
Problems with alternator belt tension (Jul 30)
Service
(Oct 8)
Gear box not working, replaced or repaired
(Nov 26)

## Slide 24: Bus 70452
The bus was unavailable to the operator for one month, undergoing full engine renovation… Immediately after a one week-long service visit!
Sep
2011
Jan
2012
Jul
2013
Jan
Gear box problems
(Nov 28)
Coolant system leak (Dec 5)
Problems with Strocco heater
(Dec 9 & Jan 30)
Tampering with EBS system (”sabotage”) Volvo Action Service
(Feb 10)
Oil pressure problems (Mar 2)
Complaints that engine „runs strangely” Probable cause: CAC leak
(Apr 12)
Service before annual inspection
(inspection
Apr 24)
Engine ”knocks”. Cylinder 1 jams during annual
inspection.
(Repair May 4)
Problems with alternator belt tension (Jul 30)
Service
(Oct 8)
Gear box not working, replaced or repaired
(Nov 26)

## Slide 25: Bus 70378
2007 model

## Slide 26: Bus 70378
2007 model
Sep
2011
Jan
2012
Jul
2013
Jan
Low oil level in gear box
(Sep 16)
Broken ECU (oil leak) and problem with urea dosing (Oct 24)
Clutch problem
(Oct 21)
Problem with Stroco heater (12 Dec, 14 Feb)
Service before annual
inspection
(inspection
Apr 17)
Coolant leak
(Feb 27)
Broken fuel pump
(Sept 21)
Service, new NOx sensor
(Oct 10)
Broken piston rod in gear box
(Sep 26)
Gear box renovation
(Nov 7)
Oil leak and broken oil level sensor
(Dec 23)
Broken modulator
(May 23)
Leak by compressor Volvo Action Service
(May 27)
Water leak in cooling system
(Jun 7)
Press guard AC broken
(Sept 19)
Coolant leak
(Nov 28)
Stroco heater
problems
(Jan 18)
Press guard AC broken
(Jul 7

## Slide 27: Bus 70378 – The Data

## Slide 28: Bus 70378
2007 model
Sep
2011
Jan
2012
Jul
2013
Jan
Low oil level in gear box
(Sep 16)
Broken ECU (oil leak) and problem with urea dosing (Oct 24)
Clutch problem
(Oct 21)
Problem with Stroco heater (12 Dec, 14 Feb)
Service before annual
inspection
(inspection
Apr 17)
Coolant leak
(Feb 27)
Broken fuel pump
(Sept 21)
Service, new NOx sensor
(Oct 10)
Broken piston rod in gear box
(Sep 26)
Gear box renovation
(Nov 7)
Oil leak and broken oil level sensor
(Dec 23)
Broken modulator
(May 23)
Leak by compressor Volvo Action Service
(May 27)
Water leak in cooling system
(Jun 7)
Press guard AC broken
(Sept 19)
Coolant leak
(Nov 28)
Stroco heater
problems
(Jan 18)
Press guard AC broken
(Jul 7

## Slide 29: Bus 70378 – The Data
The ECU was replaced on October 24
Oil leaked into the contact so that the circuit was shorted
This caused cooling fan to be running at full speed all the time

## Slide 30: Kungsbacka Results
Multiple different problems have been detected
  cylinder jam
  ECU fault resulting in cooling fan overuse
  NOx sensors
  wheel speed sensors
  wheel speed sensor modulators
But we have had limited success with compressor
  one of the reasons being not enough relevant data
  we only have access to Wet Tank Air Pressure signal

## Slide 31: Summary
Self-monitoring can reduce number of unplanned stops
  multiple serious faults have been detected early
  cylinder jams, ECU faults, NOx and wheel speed sensors
  but we have had limited success with air compressor
ReDi2Service is a generic and adaptive approach
  not directed at specific faults, making use of all available data
  develops with the life-time of the fleet, finding relevant faults
Cost efficient especially for rare and non-critical faults
  e.g. overuse of cooling fan causes fuel to be wasted
Increase overall knowledge about vehicles

## Slide 32: Summary
This requires flexible data logging and processing
  interesting individual models are found on-board
    histograms, linear relations, neural networks, …
  comparison across the fleet is done off-board
    central server or peer-to-peer architecture
What is interesting to monitor changes in time
  a single compressor replacement between 2007 and 2012
  16 compressor replacements in 2013 and 2014
Important aspect is defining the fleet to compare against
  trade-off between size (confidence) and similarity (precision)